## Slide 1: Data Errors

## Slide 2: Introduction
The processing of incorrect data can produce ridiculous and embarrassing output. Errors can take time to sort out and can be distressing to the people it affects, especially incorrect personal data.
When designing an ICT system is it essential that error checking is incorporated into the design.
We are going to look at how data errors can occur in an ICT system.

## Slide 3: Problems with Inaccurate Data
Errors can cause a variety of problems including:
Incorrect decision made resulting in a loss of money;
Goods being sent to a wrong address;
Spending time sorting our errors;
Loss of trust, confidence and goodwill;
Being prosecuted under the Data Protection Act 1998 for not keeping personal data up to date.

## Slide 4
Transcription;
Input;
Processing;
Transmission.
When Can Data Errors Occur

## Slide 5: Transcription
Transcription errors are mistakes humans make when keying in data or filling in forms.
Often occur through carelessness and not picked up with verification techniques such as proof reading.
Transcription is the process of copying data from a source document such as an order form in to an ICT system.
Careful training of staff can reduce these errors.
Validation performed by the computer program that accepts data can help, but often incorrect data is valid data which means its impossible to detect.

## Slide 6: Input
Input data even though it has been verified (i.e. checked against source documents) and validated can still be incorrect.
Incorrect data can occur in a variety of ways and is usually any human involvement at either the data collection stage or the input stage.
The way to decrease human involvement is to use direct methods of data capture such as MICR, OCR, bar coding etc. where possible.
Keyboarding can introduce a large number of errors during input.

## Slide 7: Input Cont.
Direct methods such as Optical Mark Recognition or Magnetic Ink Character Recognition can have errors.
Example: A form may not have been read correctly and marked incorrectly. If a person has filled in an OMR form incorrectly it should be rejected and the computer should not ‘guess’ what the user intended to put as this would introduce errors.

## Slide 8: Processing
Mistakes that can occur during the processing of data include:
  A programming error that remained undiscovered during testing.
  The use of a wrong data file for processing the data e.g. not using the latest file and using an older file.
  Incorrect formulas in a spreadsheet leading to information being outputted incorrectly.
  Damage by viruses – deleting data.
  Equipment malfunction – hard drives crashing, important to always back up files containing data.

## Slide 9: Transmission
When data is passed through a communication medium (wireless, cables, fibre optics) it is important the data is not corrupted on route, and if it is, that the system detects the corruption and the data is retransmitted.
Checking data after is has been transmitted along the communication line using a parity check.

## Slide 10: Parity Check Procedure
The computer adds up the number of bits in one byte and if the parity is different from the parity setting the computer will report an error.
Sending the letter C (ASCII code: 1000011)
Since there are three 1s in the code and if odd parity is being used, a 0 is added to left hand side so the total number of bits of the byte is odd. If even parity is used a 1 would be added to make it even.

## Slide 11: Parity Cont.
Communications devices have a chip to deal with parity checks; the sending device adds parity bits and the receiving device calculates what the parity bit should be. If an error occurs, parity will no longer be observed and corruption is detected.
What's the problem with this?

## Slide 12: Parity Cont.
There are two types of parity error checking - Even and Odd
Even parity is checking that the number of 1's in the data word adds up to an even number
Odd parity is checking that the number of 1's in the data word adds up to an odd number.
'Even Parity' checking can only detect an odd number of bits being corrupted (one, three etc) If the errors have caused an even number of bits to change, then parity checking cannot detect the problem.
This is why more complicated error checking schemes have been developed. But parity checks are still very common as it is such a simple way of detecting errors.

## Slide 14: Class Question
There's are a number of ways in which data errors can occur. By giving an example in each case, describe how errors can occur during:
Input (2 marks)
Transcription (2 marks)
Processing (2 marks)
Transmission (2 marks)

## Slide 15: Class Task
Research on example of direct data entry method i.e. OMR, barcodes etc.
Using the internet find an article where data errors have occurred in big businesses.